## Slide 1: Bike COACH
Olivier Avande
CYBR 8080

## Slide 2: INTRODUCTION
What is Bike Coach?
Project Goals
  Explore android application development and the IoT: Create an app integrated with BLE enabled device
    Record sensor data from MetaWear Board and process
    Simple interface displaying workout metrics
    Send feedback to user
    Test application to ensure functionality

## Slide 3: COMPONENT ARCHITECTURE
Board: MetaMotionR
Phone:
-android
-minSdk: 23
-targetSdk: 26

## Slide 4: USER STORIES
User Story 1: As a cyclist, I want to monitor my cycling performance so I can analyze and improve on my fitness
  Acceptance Criteria: A user will be able to view current speed, average speed, distance time and current temperature
User Story 2: As a cyclist, I want to set a desired speed so I can maintain that speed on my workout
  Acceptance Criteria: a user will be able to input a speed that will constitute the threshold speed he has to keep up with
User Story 3: As a cyclist, I want to receive haptic feedback so I can increase my current speed over the the specified threshold
  Acceptance Criteria: The Coin Vibe Motor of the MetaWear Board will vibrate every time the current speed is below the threshold speed

## Slide 5: USER STORIES REALISATION
User Story 1:
  Get linear acceleration from accelerometer + gyroscope values
  Offset value to calibrate acceleration value
  V(k+1) = Vk + Ak * Δt
  For each axis, find v and the total velocity equal sqrt(vx^2+vy^2+vz^2)
  Movement end check: If next 25 samples equals 0 then you stopped
  Request temperature data every 3 s from board
  Used device gps to find distance (inaccurate)
User Story 2
  Simple input box to enter speed
User Story 3
  If threshold > current vel then vibrate

## Slide 6: DEMO
AirDroid Web (http://web.airdroid.com/) > Screenshot

## Slide 7: FUTURE WORK
Bug Fix
Algorithms Improvement
Add more metrics (maybe?)
Pause button

## Slide 8: Question
?